## Slide 2: 8086 ARCHITECTURE
> The 8086 CPU is divided into two independent functional parts : BIU (Bus Interface Unit) and EU (Execution Unit) > Dividing the work between these units speed up the processing. A. THE EXECUTION UNIT (EU) > The EU of the 8086 tells the BIU where to fetch the instructions and data from, decodes instructions and executes instructions. > The EU has a 16 bit ALU which can add subtract, AND, OR, increment, decrement, complement or shift binary numbers. 1. GENERAL PURPOSE REGISTERS > The EU has eight general purpose registers, labeled AH, AL, BH, BL, CH, CL, DH and DL. > These registers can be used individually for temporary storage of 8 bit data. > The AL register is also called accumulator > It has some features that the other general purpose registers do not have. > Certain pairs of these general purpose registers can be used together to store 16 bit words. > The acceptable register pairs are AH and AL,BH and BL,CH and CL,DH and DL. > The AH-AL pair is referred to as the AX register, the BH-BL pair is referred to as the BX register, the CH-CL pair is referred to as the CX register, and the DH-DL pair is referred to as the DX register. AX = Accumulator Register BX = Base Register CX = Count Register DX = Data Register

## Slide 3
2. FLAG REGISTER > A Flag is a flip-flop which indicates some condition produced by the execution of an instruction or controls certain operations of the EU. > A 16 bit flag register in the EU contains 9 active flags. > Figure below show shows the location of the nine flags in the flag register. U = UNDEFINED CONDITIONAL FLAGS CF = CARRY FLAG [Set by Carry out of MSB] PF = PARITY FLAG [Set if Result has even parity] AF= AUXILIARY CARRY FLAG FOR BCD ZF = ZERO FLAG [Set if Result is 0] SF = SIGN FLAG [MSB of Result] OF = OVERFLOW FLAG CONTROL FLAG TF = SINGLE STEP TRAP FLAG IF = INTERRUPT ENABLE FLAG DF = STRING DIRECTION FLAG > The six conditional flags in this group are the CF,PF,AF,ZF,SF and OF. > The three remaining flags in the Flag Register are used to control certain operations of the processor. > The six conditional flags are set or reset by the EU on the basis of the result of some arithmetic or logic operation. > The Control Flags are deliberately set or reset with specific instructions you put in your program. > The three control flags are the TF, IF and DF. > Trap Flag is used for single stepping through a program. > The Interrupt Flag is used to allow or prohibit the interruption of a program. > The Direction Flag is used with string instructions.

## Slide 4
3. POINTER REGISTERS > The 16 bit Pointer Registers are IP,SP and BP respectively > SP and BP are located in EU whereas IP is located in BIU 3.1 STACK POINTER (SP) > The 16 bit SP Register provides an offset value, which when associated with the SS register (SS:SP) 3.2 BASE POINTER (BP) > The 16 bit BP facilitates referencing parameters, which are data and addresses that a program passes via the stack. > The processor combines the addresses in SS with the offset in BP. > BP can also be combined with DI and SI as a base register for special addressing. 4. INDEX REGISTERS > The 16 bit Index Registers are SI and DI 4.1 SOURCE INDEX (SI) REGISTER > The 16 bit Source Index Register is required for some string handling operations > SI is associated with the DS Register. 4.2 DESTINATION INDEX (DI) REGISTER > The 16 bit Destination Index Register is also required for some string operations. > In this context, DI is associated with the ES register. B. THE BUS INTERFACE UNIT > The BIU send out address, fetches instructions from memory, reads data from ports and memory, and writes data to ports and memory. > In other words BIU handles all transfers of data and addresses on the buses for the execution unit.

## Slide 5
1. SEGMENT REGISTERS 1.1 CODE SEGMENT REGISTER (CS) > It contains the starting address of a program's code segment. > This segment address plus an offset value in the IP register indicates the address of an instruction to be fetched for execution > For normal programming purpose, you need not directly reference this register. 1.2 DATA SEGMENT REGISTER (DS) > It contains the starting address of a program's data segment > Instruction uses this address to locate data. > This address plus an offset value in an instruction causes a reference to a specific byte location in the data segment. 1.3 STACK SEGMENT REGISTER (SS) > Permits the implementation of a stack in memory > It stores the starting address of a program's stack segment the SS register. > This segment address plus an offset value in the Stack Pointer (SP) register indicates the current word in the stack being addressed. 1.4 EXTRA SEGMENT REGISTER (ES) > It is used by some string operations to handle memory addressing. > ES Register is associated with the DI Register. 2. INSTRUCTION POINTER (IP) > The 16 bit IP Register contains the offset address of the next instruction that is to execute. > IP is associated with CS register as (CS:IP) > For each instruction that executes, the processor changes the offset value in IP so that IP in effect directs each step of execution. 3. THE QUEUE > While the EU is decoding an instruction or executing an instruction which does not require use of the buses, the BIU fetches up to six instructions bytes for the following instructions. > The BIU Stores pre-fetched bytes in First in First out register set called a queue. > When the EU is ready for its next instruction, it simply reads the instruction bytes for the instruction from the queue in the BIU. > This is much faster than sending out an address to the system memory and waiting for memory to send back the next instruction byte or bytes. > Fetching the next instruction while the current instruction executes is called pipelining.

## Slide 6: ADDRESSING MODES
> The different ways in which a processor can access data are referred to as its addressing modes. > In assembly language statements, the addressing mode is indicated in the instruction itself. > The various addressing modes are 1. REGISTER ADDRESSING MODE > It is the most common form of data addressing. > Transfers a copy of a byte/word from source register to destination register. > It is carried out with 8 bit registers AH,AL,BH,BL,CH,CL,DH & DL or with 16 bit registers AX,BX,CX,DX,SP,BP,SI and DI. > It is important to use registers of same size. > Never mix an 8 bit register with a 16 bit register i.e. MOV AX, BL EXAMPLES MOV AL, BL : Copies BL into AL MOV ES, DS : Copies DS into ES MOV AX, CX : Copies CX into AX 2. IMMEDIATE ADDRESSING MODE > The term immediate implies that the data immediately follow the hexadecimal opcode in the memory. > Note that immediate data are constant data. > It transfers the source immediate byte/word of data in destination register or memory location. EXAMPLES MOV AL, 90 : Copies 90 into AL MOV AX, 1234H : Copies 1234H into AX MOV CL, 10000001B : Copies 100000001 binary value into CL

## Slide 7
3. DIRECT ADDRESSING MODE > In this scheme, the address of the data is defined in the instruction itself. > When a memory location is to be referenced, its offset address must be specified EXAMPLES MOV AL, [1234H] MOV AL, NUMBER 4. REGISTER INDIRECT ADDRESSING MODE > Register Indirect Addressing allows data to be addressed at any memory location through an offset address held in any of the following registers: BP, BX, DI and SI. > It transfers byte/word between a register and a memory location addressed by an index or base registers. > The symbol [ ] denote indirect addressing. EXAMPLES MOV CX, [BX] MOV [DI], BH MOV [DI], [BX] 5. BASE PLUS INDEX ADDRESSING MODE > Base plus index addressing is similar to indirect addressing because it indirectly addresses memory data. > This type of addressing uses one base register (BP or BX) and one Index Register (DI or SI) to indirectly address memory. EXAMPLES MOV CX, [BX+DI] MOV CH, [BP+SI]

## Slide 8
6. REGISTER RELATIVE ADDRESSING MODE > In this case, the data in a segment of memory are addressed by adding the displacement to the content of base or an index register (BP, BX ,DI or SI). > Transfers a byte/word between a register and the memory location addressed by an index or base register plus a displacement. EXAMPLES MOV [SI+4], BL 7. BASE RELATIVE PLUS INDEX ADDRESSING MODE > The base relative plus index addressing mode is similar to the base plus index addressing mode but it adds a displacement to form a memory address. > Transfers a byte or word between a register and the memory location addressed by a base and an index register plus a displacement. EXAMPLES MOV DH, [BX+DI+20H]

## Slide 9: ASSEMBLY LANGUAGE PROGRAM DEVELOPMENT TOOLS
1. EDITOR > An Editor is a Program which allows you to create a file containing the Assembly Language statements for your Program. 2. ASSEMBLER > An Assembler Program is used to translate the assembly language mnemonics for instruction to the corresponding binary codes. 3. LINKER > A Linker is a Program used to join several files into one large .obj file. It produces .exe file so that the program becomes executable. 4. LOCATOR > A Locator is a program used to assign the specific address of where the segment of object code are to be loaded into memory. > It usually converts .exe file to .bin file. 5. DEBUGGER > A Debugger is a program which allows you to load your .obj code program into system memory, execute program and troubleshoot. > It allows you to look at the content of registers and memory locations after your program runs. > It allows to set the breakpoint. 6. EMULATOR > An Emulator is a mixture of hardware and software. > It is used to test and debug the hardware and software of an external system such as the prototype of a Microprocessor based system.

## Slide 10: TYPES OF ASSEMBLER
1. One Pass Assembler > This assembler goes through or scans the assembly language program once and translates the assembly language program into binary codes. > This assembler has the program of defining forward references i.e a JUMP instruction using an address that appears later in the program must be defined by the programmer. 2. Two Pass Assembler > This assembler goes through or scans the assembly language program twice. > In the first scan, the assembler the table of symbols which consists of labels with their corresponding addresses. > In second scan, the assembler translates the assembly language program into the binary codes. > No address calculations are needed to be done by the programmer for JUMP instructions. > It is more efficient and easier to use. MACRO ASSEMBLER A macro assembler translates a program written in macro language into the binary codes (machine language). A macro language is the one in which all the instruction sequences can be defined using macros. A macro is an instruction sequence having specific name that appears repeatedly in a program. The macro assembler replaces a macro name with the appropriate instructions sequence, each time it encounters a macro name.

## Slide 11: ASSEMBLER DIRECTIVES
> Assembly Language supports a number of statements that enable to control the way in which a source program assembles and lists. These Statements are called Directives. > They act only during the assembly of a program and generate no machine executable code. > The most common Directives are: 1. PAGE DIRECTIVE > The PAGE Directive helps to control the format of a listing of an assembled program. > It is optional Directive. > At the start of program, the PAGE Directive designates the maximum number of lines to list on a page and the maximum number of characters on a line. > Its format is PAGE [LENGTH],[WIDTH] > Omission of a PAGE Directive causes the assembler to set the default value to PAGE 50,80 2. TITLE DIRECTIVE > The TITLE Directive is used to define the title of a program to print on line 2 of each page of the program listing. > It is also optional Directive. > Its format is TITLE [TEXT] EXAMPLE TITLE "PROGRAM TO PRINT FACTORIAL NO" 3. SEGMENT DIRECTIVE > The SEGMENT Directive defines the start of a segment. > A Stack Segment defines stack storage, a data segment defines data items and a code segment provides executable code. > The format (including the leading dot) for the directives that defines the stack, data and code segment are- .STACK [SIZE] .DATA ........ Initialize Data Variables .CODE > Default Stack size is 1024 bytes. > To use them as above, Memory Model initialization should be carried out. .

## Slide 12
4. MEMORY MODEL DEFINTION > The different models tell the assembler how to use segments to provide space and ensure optimum execution speed. > The format of Memory Model Definition is-
5. THE PROC DIRECTIVE > The Code Segment contains the executable code for a program, which consists of one or more procedures, defined initially with the PROC Directive and ended with the ENDP Directive. > Format is given as: PROCEDURE NAME PROC ........ ........ ........ PROCEDURE NAME ENDP 6. END DIRECTIVE > As already mentioned, the ENDP Directive indicates the end of a procedure. > An END Directive ends the entire Program and appears as the last statement. > Its Format is END [PROCEDURE NAME] 7. THE EQU DIRECTIVE > It is used for redefining symbolic names EXAMPLE DATAX DB 25 DATA EQU DATAX 8. THE .STARTUP AND .EXIT DIRECTIVE > MASM 6.0 introduced the .STARTUP and .EXIT Directive to simplify program initialization and Termination. > .STARTUP generates the instruction to initialize the Segment Registers. > .EXIT generates the INT 21H function 4ch instruction for exiting the Program.

## Slide 13: MODULAR PROGRAMMING
1. LINKING AND RELOCATION Program is composed from several smaller modules. Modules could be developed by separate teams concurrently. The modules are assembled producing .OBJ modules (Object modules). The DOS linking program links the different object modules of a source program and function library routines to generate an integrated executable code of the source program. The main input to the linker is the .OBJ file that contains the object modules of the source programs. The linker program is invoked using the following options. C> LINK or C>LINK MS.OBJ The .OBJ extension is a must for a file to be accepted by the LINK as a valid object file. The first object may generate a display asking for the object file, list file and libraries as inputs and an expected name of the .EXE file to be generated. The output of the link program is an executable file with the entered filename and .EXE extension. This executable filename can further be entered at the DOS prompt to execute the file. Linking is necessary because of the number of codes to be linked for the final binary file. The linked file in binary for run on a computer is commonly known as executable file or simply '.exe' file. After linking, there has to be re-allocation of the sequences of placing the codes before actually placement of the codes in the memory. The loader program performs the task of reallocating the codes after finding the physical RAM addresses available at a given instant. The loader is a part of the operating system and places codes into the memory after reading the '.exe' file. This step is necessary because the available memory addresses may not start from 0x0000, and binary codes have to be loaded at the different addresses during the run. The loader finds the appropriate start address. In a computer, the loader is used and it loads a program that is ready to run, into a section of RAM. A program called locator reallocates the linked file and creates a file for permanent location of codes in a standard format.

## Slide 14
2. STACK > The stack is a block of memory that may be used for temporarily storing the contents of the registers inside the CPU. > It is a top-down data structure whose elements are accessed using the stack pointer (SP) which gets decremented by two as we store a data word into the stack and gets incremented by two as we retrieve a data word from the stack back to the CPU register. > The process of storing the data in the stack is called 'pushing into' the stack and the reverse process of transferring the data back from the stack to the CPU register is known as 'popping off' the stack. > The stack is essentially Last-In-First-Out (LIFO) data segment. This means that the data which is pushed into the stack last will be on top of stack and will be popped off the stack first. > The stack pointer is a 16-bit register that contains the offset address of the memory location in the stack segment. Stack Segment register (SS) contains the base address of the stack segment in the memory. 3. PROCEDURES/SUBROUTINES > Procedure or a subroutine or a function is a key concept for modular programming, the essential way to reduce complexity. > A procedure is a reusable set of instructions that has a name. > Only one copy of the procedure is stored in the memory; and it can be called as many times as needed. > only one copy is stored, it saves memory; but has execution time overhead for the. CALL and RETURN operations. > CALL transfers control to the procedure just like in JUMP; but unlike a JUMP, procedure has a RETURN instruction which returns control to the instruction following the CALL instruction > In order to implement such a return, the necessary information is stored on a stack, before transferring control to the procedure. > In program, procedure starts with PROC directive and ends with ENDP directive. > PROC directive is followed by the type of procedure: NEAR or FAR.

## Slide 15
3.1 Calling a Procedure > CALL instruction followed by procedure name is used in a program to call a procedure. > Procedure calls are of two types: Near CALL and Far CALL. Near CALL > A procedure may be in the same code segment as that of the main program (Intra segment). In such a case, we specify only IP. This is known as NEAR CALL. Example: Main program: .... .... CALL DISPLAY ; calling a procedure. .... .... Procedure Definition.... DISPLAY PROC NEAR MOV DX, OFFSET string1 MOV AH, 02H INT 21H RET DISPLAY ENDP FAR CALL > A procedure may be in a different code segment (Inter segment). In such a case, we need to specify both IP and CS (directly or indirectly). This is known as a FAR CALL. Example: DISPLAY PROC FAR . . . . . . DISPLAY ENDP Now, a CALL to DISPLAY is assembled as FAR CALL.

## Slide 16
4. MACRO > MACRO is a group of instructions with a name. > When a macro is invoked, the associated set of instructions replaces the macro name in the program. This macro expansion is done by a Macro Assembler and it happens before assembly. Thus the actual Assembler sees the expanded source. MACRO Definition: A macro has a name. The body of the macro is defined between a pair of directives, MACRO and ENDM. Examples of Macro Definitions: DISPLAY MACRO ; Definition of a Macro named DISPLAY MOV DX, OFFSET string1 MOV AH, 09H INT 21H ENDM ; end of Macro MACROS Vs PROCEDURES 1) Procedure: > Only one copy exists in memory. Thus memory consumed is less. > Called when required. > Return address (IP or CS:IP) is saved (PUSH) on stack before transferring control to the subroutine through CALL instruction. It should be popped (POP) again when control comes back to calling program with RET instruction. > Execution time overhead is present because of the call and return instructions. > If more lines of code, better to write a procedure than a macro. 2) Macro: > When a macro is invoked, the corresponding code is inserted into the source. Thus multiple copies of the same code exist in the memory leading to greater space requirements. > However, there is no execution overhead because there are no additional call and return instructions. > No use of stack for operation. > Good if few lines of code are in the Macro body.

## Slide 17: 8086 INTERRUPTS
> An 8086 interrupt can come from any one of 3 sources. > One source is an external signal applied to the Nonmaskable Interrupt (NMI) or to the (INTR) input pin. An interrupt caused by a signal applied to one of these inputs (NMI or INTR) is referred as Hardware Interrupt. > A second source of an interrupt is execution of the interrupt instruction INT nn. This is referred as Software Interrupt. > The third source of an interrupt is some error conditions produced in 8086, by the execution of an instruction, referred as processor interrupt. INTERRUPT VECTOR TABLE (IVT) > 8086 consists of 256 interrupts stored from memory location 00000H to 003FFH i.e. 1024 Bytes (1KB) of memory. > These 256 interrupts are stored in memory location forming a table which is called Interrupt Vector Table (IVT). > An Interrupt Vector contains the address (segment CS and offset IP) of the Interrupt Service Routine. > Each vector is a 4 byte long and contains the starting address of the Interrupt Service Routine. > The first 2 bytes of the vector contain the offset address (IP) and the last two bytes contain the segment address (CS). 8086 PREDEFINED INTERRUPT TYPES 1. DIVIDE BY ZERO INTERRRUPT: TYPE 0 > Divide error occurs when the result of division overflow or whenever an attempt is made to divide by zero. > The 8086 type 0 is automatic and cannot be disabled in any way 2. SINGLE STEP INTERRUPT : TYPE 1 > If the 8086 trap flag is set, the 8086 will automatically do a type 1 interrupt after each instruction executes. > When a MP is interrupted using Type 1 interrupt, it will execute one instruction and stop so that we can then examine the contents of registers and memory locations. > In other words, in single step mode, a system will stop after it executes each instruction and waits for further direction from us.

## Slide 18
3. NON MASKABLE INTERRUPT : TYPE 2 > A result of placing logic 1 on the NMI input pin causes type 2 interrupt. > This input is non-maskable, which means that it cannot be disabled. > Another common use of type 2 interrupt is to save program data in case of a system power failure or to deal with some other catastrophic failure conditions. > Some external circuitry detects when the AC power to the system fails and sends an Interrupt signal to the NMI. 4. BREAKPOINT INTERRUPT : TYPE 3 > Used to insert a breakpoint into the program. When a break point is inserted, the system executes the instructions up to the breakpoint, and then stops execution. > The INT 3 instruction is often used to store a breakpoint in a program for debugging. 5. OVERFLOW INTERRUPT : TYPE 4 > A special vector used with the INTO instruction. > The 8086 overflow flag, OF, will be set if the signed result of an arithmetic operation on two signed numbers is too large to be represented in the destination register or memory location. > The INTO instruction interrupts the program if an overflow condition exists as reflected by overflow flag (OF).