## Slide 1: SERIAL AND PARALLEL DATA TRANSFER

## Slide 4
A. Parallel Data Transfer Defination: Within a computing or communication device, the distances between different subunits are too short. Thus, it is normal practice to transfer data between subunits using a separate wire to carry each bit of data. There are multiple wires connecting each sub-unit and data is exchanged using a parallel transfer mode. This mode of operation results in minimal delays in transferring each word. > In parallel data transfer, all the bits of data are transmitted simultaneously on separate communication lines. > In order to transmit n bits, n wires or lines are used. Thus each bit has its own line. > All n bits of one group are transmitted with each clock pulse from one device to another i.e. multiple bits are sent with each clock pulse. > Parallel data transfer is used for short distance communication. > As shown in the fig, eight separate wires are used to transmit 8 bit data from sender to receiver. Advantage of parallel data transfer It is speedy way of transmitting data as multiple bits are transmitted simultaneously with a single clock pulse. Disadvantage of parallel data transfer It is costly method of data data transfer as it requires n lines to transmit n bits at the same time.

## Slide 5
B. Serial Data Transfer Defination: When transferring data between two physically separate devices, especially if the separation is more than a few kilometers, for reasons of cost, it is more economical to use a single pair of lines. Data is transmitted as a single bit at a time using a fixed time interval for each bit. This mode of data transfer is known as bit-serial data transfer. > In serial data transfer, the various bits of data are transmitted serially one after the other. > It requires only one communication line rather than n lines to transmit data from sender to receiver. > Thus all the bits of data are transmitted on single line in serial fashion. > In serial data transfer, only single bit is sent with each clock pulse. > As shown in figure suppose an 8-bit data 11001010 is to be sent from source to destination. Then least significant bit (LSB) i,e. 0 will be transmitted first followed by other bits. The most significant bit (MSB) i.e. 1 will be transmitted in the end via single communication line. > The internal circuitry of computer transmits data in parallel fashion. So in order to change this parallel data into serial data, conversion devices are used. > These conversion devices convert the parallel data into serial data at the sender side so that it can be transmitted over single line. > On receiver side, serial data received is again converted to parallel form so that the interval circuitry of computer can accept it. > Serial data transfer is used for long distance communication. Advantage of Serial Data Transfer Use of single communication line reduces the data transfer line cost by the factor of n as compared to parallel data transfer. Disadvantages of Serial Data Transfer 1. Use of conversion devices at source and destination end may lead to increase in overall data transfer cost. 2. This method is slower as compared to parallel data transfer as bits are transmitted serially one after the other.

## Slide 6
TYPES OF SERIAL DATA TRANSFER There are two types of serial data transfer: Synchronous and Asynchronous, both these data transfers use 'Bit synchronization' Bit Synchronization is a function that is required to determine when the beginning and end of the data data transfer occurs. Bit synchronization helps the receiving computer to know when data begin and end during a data transfer. Therefore bit synchronization provides timing control. Asynchronous Data Transfer > Asynchronous data transfer sends only one character at a time where a character is either a letter of the alphabet or number or control character i.e. it sends one byte of data at a time. > Bit synchronization between two devices is made possible using start bit and stop bit. > Start bit indicates the beginning of data i.e. alerts the receiver to the arrival of new group of bits. A start bit usually 0 is added to the beginning of each byte. > Stop bit indicates the end of data i.e. to let the receiver know that byte is finished, one or more additional bits are appended to the end of the byte. These bits, usually 1s are called stop bits. > Addition of start and stop increase the number of data bits. Hence more bandwidth is consumed in asynchronous data transfer. > There is idle time between the data transfers of different data bytes. This idle time is also known as Gap. > The gap or idle time can be of varying intervals. This mechanism is called Asynchronous, because at byte level sender and receiver need not to be synchronized. But within each byte, receiver must be synchronized with the incoming bit stream. Application of Asynchronous data transfer

## Slide 7
Asynchronous data transfer is well suited for keyboard type-terminals and paper tape devices. The advantage of this method is that it does not require any local storage at the terminal or the computer as data transfer takes place character by character. 2. Asynchronous data transfer is best suited to Internet traffic in which information is transmitted in short bursts. This type of data transfer is used by modems.
Advantages of Asynchronous data transfer 1. This method of data data transfer is cheaper in cost as compared to synchronous e.g. If lines are short, asynchronous data transfer is better, because line cost would be low and idle time will not be expensive. 2. In this approach each individual character is complete in itself, therefore if character is corrupted during data transfer, its successor and predecessor character will not be affected. 3. It is possible to transmit signals from sources having different bit rates. 4. The data transfer can start as soon as data byte to be transmitted becomes available. 5. Moreover, this mode of data data transfer in easy to implement. Disadvantages of Asynchronous data transfer 1. This method is less efficient and slower than synchronous data transfer due to the overhead of extra bits and insertion of gaps into bit stream. 2. Successful data transfer inevitably depends on the recognition of the start bits. These bits can be missed or corrupted.

## Slide 8
Synchronous Data Transfer > Synchronous data transfer does not use start and stop bits. > In this method bit stream is combined into longer frames that may contain multiple bytes. > There is no gap between the various bytes in the data stream. > In the absence of start & stop bits, bit synchronization is established between sender & receiver by 'timing' the data transfer of each bit. > Since the various bytes are placed on the link without any gap, it is the responsibility of receiver to separate the bit stream into bytes so as to reconstruct the original information. > In order to receive the data error free, the receiver and sender operates at the same clock frequency. Application of Synchronous data transfer > Synchronous data transfer is used for high speed communication between computers. Advantage of Synchronous data transfer 1. This method is faster as compared to asynchronous as there are no extra bits (start bit & stop bit) and also there is no gap between the individual data bytes. Disadvantages of Synchronous data transfer 1. It is costly as compared to asynchronous method. It requires local buffer storage at the two ends of line to assemble blocks and it also requires accurately synchronized clocks at both ends. This lead to increase in the cost. 2. The sender and receiver have to operate at the same clock frequency. This requires proper synchronization which makes the system complicated.

## Slide 9
Key Differences Between Serial And Parallel Transmission
Serial transmission requires a single line to communicate and transfer data whereas, parallel transmission requires multiple lines.
Serial transmission is used for long-distance communication. As against, parallel transmission is used for the shorter distance.
Error and noise are least in serial as compared to parallel transmission. Since one bit follows another in Serial Transmission whereas, in Parallel Transmission multiple bits are sent together.
Parallel transmission is faster as the data is transmitted using multiples lines. On the contrary, in Serial transmission data flows through a single wire.
Serial Transmission is full-duplex as the sender can send as well as receive the data. In contrast, Parallel Transmission is half-duplex since the data is either sent or received.
The special types of converters are required in a serial transmission system to convert the data between the internal parallel form and serial form while there is no such requirement of converters in parallel transmission systems.
Serial transmission cables are thinner, longer and economical in comparison with the Parallel Transmission cables.
Serial Transmission is simple and reliable. Conversely, Parallel Transmission is unreliable and complicated

## Slide 10
Key Differences Between Synchronous and Asynchronous Transmission
In Synchronous Transmission, data is transferred in the form of frames. On the other hand, in Asynchronous Transmission data is transmitted 1 byte at a time.
Synchronous Transmission requires a clock signal between the sender and receiver so as to inform the receiver about the new byte. In contrast, in Asynchronous Transmission sender and receiver does not require a clock signal as the data sent here has a parity bit attached to it which indicates the start of the new byte.
Data transfer rate of Asynchronous Transmission is slower than that of Synchronous Transmission.
Asynchronous Transmission is simple and economical, whereas Synchronous Transmission is complicated and expensive.
Synchronous Transmission is efficient and has lower overhead as compared to the Asynchronous Transmission.
In asynchronous data transfer, the line is kept at a stable value (logic 1) if no data is transmitted through the line. As against, in synchronous transfer, the end of the data is indicated by the sync character(s). Further than the sync characters, the line can be either high or low.

## Slide 11
METHODS OF PARALLEL DATA TRANSFER Simple Input and Output When you need to get digital data from a simple switch, such as a thermostat, into a microprocessor, all you have to do is connect the switch to an input port line and read the port. The thermostat data is always present and ready, so you can read it at any time. Likewise, when you need to output data to a simple display device such as an LED, all you have to do is connect the input of the led buffer on an output port pin and output the logic level required to turn on the light. The LED is always there and ready, so you can send data to it at any time. The timing waveform for this situation is shown below. The crossed lines on the waveform represents the time at which new data byte becomes valid on the output lines of the port. The absence of other waveform indicates that this output operation is not directly dependent on any other signals. Simple Strobe IO In many applications, valid data is present on an external device only at a certain time, so it must be read in at that time. An example of this is an ASCII-encoded keyboard. When a key is pressed, circuitry on the keyboard sends out the ASCII code for the pressed key on eight parallel data lines, and then sends out a strobe signal (STB') on another line to indicate that valid data is present on the eight data lines. We can connect this strobe line to an input port line and poll it to determine when we can input valid data from keyboard. Another way is to connect this strobe line to interrupt input on the processor and have an Interrupt Service Routine to read in the data when the processor receives and interrupt. Figure below shows the timing waveform which represents this type of operation. The sending device, such as keyboard, outputs parallel data on the data lines and then outputs an STB' signal to let us know that valid data is present.

## Slide 12
For low rates of data transfer, such as from keyboard to microprocessor, a simple strobe transfer works well. However, for higher speed data transfer this method does not work, because there is no signal which tells the sending device when it is safe to transfer the next data byte. In other words, the sending device can send data faster then the receiving system could read them. To prevent this problem, a handshake data transfer scheme is used. Single Handshake IO Figure below shows the circuit connections and timing waveform for a handshake data transfer from a peripheral device to a microprocessor. The peripherals outputs some parallel data and sends an STB' signal to the microprocessor. The microprocessor detects the asserted STB' signal on a polled or interrupt basis and reads in the data byte. Then the microprocessor sends an Acknowledgement signal (ACK) to the peripheral to indicate that the data has been read and the peripheral can send the next byte of data. From the viewpoint of microprocessor, this operation is referred to as a handshake input. These same waveforms might represent a handshake output from a microprocessor to a parallel printer. In this case, the microprocessor outputs a character to the printer and asserts STB' signal to the printer to tell the printer, " Here is the character for you." When the printer is ready it answers back with the ACK signal to tell the microprocesor, "I got that one; send me another." The point of this handshake scheme is that the sending device or system is designed so that it does not send the next data byte until the receving device or system indicates with an ACK signal that it is ready to receive next byte.

## Slide 13
Double Handshake Data Transfer The data transfer where more coordination is required between sending and receiving system, a double handshake is used. The circuit connections are same as that of single handshake as shown above. The figure below shows a waveform for a double handshake input from a peripheral to a microprocessor. Perhaps it will help us follow these waveforms by thinking of them as a conversation between two people. In these waveforms, each signal edge has meaning. The sending device asserts its STB' line low to ask, "Are you ready?" The receiving system raises its ACK line high to say "I'm ready." The peripheral device then sends the byte of data and raises its STB' line high to say, "Here is some valid data for you." After it has read in the data, the receiving device drops its ACK line low to say, "I have that data, thank you, and I wait your request to send the next byte of data." For a handshake output of this type, from a microprocessor to a peripheral, the waveforms are the same, but the microprocessor sends the STB' signal and the data, and the peripheral sends the ACK signal.