## Slide 1: Instruction Format:
An instruction format defines the layout of the bits of an instruction, in terms of its constituents parts.
An instruction format must include an opcode and, implicitly or explicitly, zero or more operands. Each explit operand is referenced using one of the addressing mode that is available for that machine.
The format must, implicitly or explictly, indicate the addressing mode of each operand.
For most instruction sets, more than one instruction format is used.

## Slide 2: INSTRUCTION FORMAT
An instruction (instruction format) is a command to the microprocessor to perform a given task on a particular data. Each instruction (instruction format) is of two parts. One is task to be performed, called the operation code or opcode and the second one is the data to be operated on, called the operand. The operands or data can be specified in different ways. It may include an 8-bit or 16-bit data, an internal register. a memory location, or 8-bit or 16-bit address. In some instructions, the operand is implicit.
Instruction Word Size
The 8085 instruction set is of three groups according to word size:
One-word or one-byte instructions.
Two-word or two-byte instructions.
Three-word or three-byte instructions.
In the 8085 microprocessor, byte and words are synonymous because it is an 8-bit microprocessor. But, instructions are commonly referred to in terms of bytes rather than words.
One-byte instructions
A one-byte instruction includes a opcode and a operand in the same byte. Operand(s) are internal registers and are in the instruction in form of codes. If there is no numeral present in the instruction then that instruction will be of one-byte, for example, MOV C, A, RAL, and ADD B, etc.

## Slide 3
Two-byte instructions
In a two-byte instruction, the first byte specifies the operation code and second byte specifies the operand. Source operand is a data byte and immediately following the opcode.
If an 8-bit numeral is present in the instruction then that instruction will be of two-byte. Here, the numeral may be a data or an address.
For example, in MVI A, 35H and MVI B, 29H, etc.
In a two-byte instruction, the first byte will be the opcode and the second byte will be for the numeral present in the instruction.

## Slide 4
Three-byte instructions
In a three-byte instruction, the first byte specifies the opcode, and the following two bytes specify the 16-bit operand.
The second byte is the low-order operand and the third byte is the high-order operand.
If a 16-bit numeral is present in the instruction then that instruction will be of three-byte.
Here, the numeral may be a data or an address, for example, in LDA 2080H and STA 2500H, etc.

## Slide 5: Opcode Format
In the case of microprocessor, the instruction or operation are specified by using specific bit pattern unique for each instruction.
These bit patterns contain all the information about operation, register used, memory to. The register and register pair are specified by using certain combination of bits.
For eg: Register B, C,D,E, BC,DE,etc.

## Slide 6: 8085 ADDRESSING MODES
The ways by which operands are specified in an instruction are called addressing modes. The different addressing modes of 8085 are:
1. Immediate Addressing Mode
If the data is present within the instruction itself, then it is called immediate addressing mode.
Examples: MVI A, 05H
ADI 55H
LXI H, C000H
2. Register Addressing Mode
If the data is present in the register and the register are specified in an instruction, than it is called register addressing mode.
Examples: MOV A, B
ADD B
ANA C

## Slide 7
3. Direct Addressing Mode
If the address of the data is specified in the instruction itself, than it is called direct addressing mode.
Examples: LDA 2000H
STA 2000H
IN 10H
OUT 01H
4. Register Indirect Addressing Mode
If the register pair which contains the address of the data is specified in the instruction, than it is called register indirect addressing mode.
Examples: LDAX B
STAX D
MOV M, A
MOV B, M

## Slide 8
5. Implied Addressing Mode
If the opcode in an instruction tells about the operand, than it is called implied addressing mode.
Examples: RAL
RRC

## Slide 9: Instructions set of 8085
An instruction is a binary pattern designed inside a microprocessor to perform a specific function.
The entire group of instructions that a microprocessor supports is called Instruction Set.
8085 has 246 instructions.
Each instruction is represented by an 8-bit binary value.
These 8-bits of binary value is called Op-Code or Instruction Byte

## Slide 10: Classification of Instruction Set
• Data Transfer Instruction
• Arithmetic Instructions
• Logical Instructions
• Branching Instructions
• Control Instructions

## Slide 11: Data Transfer Instructions
MOV Rd, Rs
> Copies the content of source register Rs into destination register Rd
> Rs and Rd can be A, B, C, D, E, H, L
MOV A, B
MOV M, Rs
> Copies the content of register Rs into memory location M
> Rs can be A, B, C, D, E, H, L
> The memory location M is specified by HL pair
MOV M, A

## Slide 12
MOV Rd, M
> Copies the content of memory location M into register Rd
> Rd can be A, B, C, D, E, H, L
> The memory location M is specified by HL pair
MOV A, M
MVI Rd, 8-bit
> The 8-bit data is stored in the destination register Rd
> Rd can be A, B, C, D, E, H, L
MVI A, 32H

## Slide 13
MVI M, 8-bit
> The 8-it data is stored in memory location M
> M is specified by HL pair
MVI M, 32H
LDA 16-bit
> Copies the content of memory location specified by 16-bit address into A
LDA 2015H

## Slide 14
STA 16-bit
> Copies the content of A into 16-bit memory address
STA 2015H
LDAX Rp
> Copies the content of memory location specified by register pair Rp into A
> Rp can be B or D i.e. BC pair or DE pair
LDAX D

## Slide 15
STAX Rp
> Copies the content of A into 16-bit memory address specified by Rp
> Rp(Register Pair) can be B or D i.e. BC pair or DE pair
STAX D
LXI Rp, 16-bits
> Loads 16-bit data into register pair
> Rp can be B, D or H i.e. BC pair, DE pair or HL pair
LXI H, 2072H

## Slide 16
IN 8-bit
> The data from i/p port specified by 8-bit address is transferred into A
IN 40H
OUT 8-bit
> The data of A is transferred into output port specified by 8-bit address
OUT 40H

## Slide 17
XCHG
> Exchange the content of HL pair with DE pair
i.e. the content of H and D are exchanged whereas
content of L and E are exchanged
XCHG

## Slide 18: Arithematic Instructions
ADD R/M
> The content of register /memory (R/M) is added to the A
> Result is stored in A
> The memory M is specified by HL pair
ADD B
ADD M
ADC R/M
> The content of register /memory (R/M) is added to the A along with carry flag CF
> The result is stored in A
> The memory M is specified by HL pair
ADC B
ADC M

## Slide 19
ADI 8-Bit
> The 8-bit data is added to A and result is stored in A
ADI 32H
ACI 8-Bit
> The 8-bit data is added to A along with carry flag CF
> The result is stored in A
ACI 32H

## Slide 20
SUB R/M
> The content of register /memory (R/M) is subtracted from A
> The result is stored in A
> The memory M is specified by HL pair
SUB C
SUB M
SBB R/M
> The content of register /memory (R/M) is subtracted from A along with borrow flag BF
> The result is stored in A
> The memory M is specified by HL pair
SBB B
SBB M

## Slide 21
SUI 8-Bit
> The 8-bit data is subtracted from A and result is stored in A
SUI 32H
INC R/M
> Increment the content of register/memory by 1
> Memory is specified by HL pair
INC B
INC M

## Slide 22
DCR R/M
> Decrement the content of register/memory by 1
> Memory is specified by HL pair
DCR B
DCR M
INX Rp
> Increment the content of register pair Rp by 1
INX H
DCX Rp > Decrement the content of register pair Rp by 1 DCX H

## Slide 23: Logical Instructions
CMP R/M
(Compare Register/Memory)
> Compares the content of register/memory with A
> The result of comparison is:
If A< R/M : Carry Flag CY=1
If A= R/M : Zero Flag Z=1
If A> R/M : Carry Flag CY=0
CMP B
CMP M

## Slide 24
CPI 8-bit
(Compare Immediate)
> Compares 8-bit data with A
> The result of comparison is:
If A< 8-bit : Carry Flag CY=1
If A= 8-bit : Zero Flag Z=1
If A> 8-bit : Carry Flag CY=0
CPI 32H

## Slide 25
ANA R/M
(logical AND register/memory)
> The content of A are logically ANDed with the content of register/memory and result is stored in A
> Memory M must be specified by HL pair
ANA B
ANA M

## Slide 26
ANI 8-bit
(Compare Immediate)
> The content of A are logically ANDed with the 8-bit data and result is stored in A
ANI 32H
ORA R/M
(logical OR register/memory)
> The content of A are logically ORed with the content of register/memory and result is stored in A
> Memory M must be specified by HL pair
ORA B
ORA M

## Slide 27
ORI 8-bit
(OR immediate)
> The content of A are logically ORed with the 8-bit data and result is stored in A
ORI 32H
XRA R/M
(logical XOR register/memory)
> The content of A are logically XORed with the content of register/memory and result is stored in A
> Memory M must be specified by HL pair
XRA B
XRA M

## Slide 28
XRI 8-bit
(XOR immediate)
> The content of A are logically XORed with the 8-bit data and result is stored in A
XRI 32H
RLC
(Rotate Accumulator Left)
> Each bit of A is rotated left by one bit position.
> Bit D7 is placed in the position of D0.
RLC

## Slide 29
RRC
(Rotate Accumulator Right)
> Each bit of A is rotated right by one bit position.
> Bit D0 is placed in the position of D7.
RRC
RAL
(Rotate Accumulator Left with Carry)
> Each bit of A is rotated left by one bit position along with carry flag CY
> Bit D7 is placed in CY and CY in the position of D0.
RAL

## Slide 30
RAR
(Rotate Accumulator Right with Carry)
> Each bit of A is rotated right by one bit position along with carry flag CY.
> Bit D7 is placed in CY and CY in the position of D0.
RAR

## Slide 31: Branching Instructions
JMP 16-bit
(Unconditional Jump)
The program sequence is transferred to the memory location
specified by 16-bit address
JMP C000H

## Slide 32
JC
Jump on Carry (CY=1)
JNC
Jump on No Carry (CY=0)
JP
Jump on Positive (S=0)
JM
Jump on Negative (S=1)
JZ
Jump on Zero (Z=1)

## Slide 33
JNZ
Jump on No Zero (Z=0)
JPE
Jump on Parity Even (P=1)
JPO
Jump on Parity Odd (P=0)

## Slide 34
CALL 16-bit
The program sequence is transferred to the subroutine at
memory location specified by the 16-bit address
CALL C000H
RET
The program sequence is transferred from the subroutine
program to calling program
RET

## Slide 35: Machine Control Instructions
NOP
No operation is performed.
NOP
HLT
The CPU finishes executing the current instruction and stops any further execution
HLT

## Slide 36: ASSIGNMENT 2
1. What do you mean by addressing modes? Explain 8085 addressing modes. 2. Identify size, adressing mode, machine cycles and functions of following 8085 instructions: MVI A, 32H LDA 1234H STAX D MOV M, B RLC MOV B, C ADI 40H LXI H, 1234H 3. Draw timing diagram for the following 8085 instructions and also determine the time taken to execute the instruction if the clock frequency of 8085 is 10MHz. MVI A, 32H LDA 2072H STA 2073H IN 40H OUT 50H LXI H, 1234H 4. What do you mean by instruction cycle, machine cycle and T-states.

## Slide 37
5. Write 8085 ALP to transfer 10 bytes of data starting from memory location 2070H to memory locations starting from 2080H. 6. Write 8085 ALP to count number of 1’s in a given byte of data. 7. Write 8085 ALP to count number of negative numbers stored in an array of 30 bytes stored in memory location starting from 2072H. 8. Write 8085 ALP to multiply any two bytes and store result in memory locations starting from C000H. 9. Write 8085 ALP to check whether the content of memory location AAAAH is odd or even. If it is odd store 00H in memory location AAABH else store FFH in AAACH. 10. Write 8085 ALP to find the factorial of a number.